## Slide 1: Using Polycom at Southern Wesleyan
Presented by
Mike Preusz

## Slide 2: Introduction
This training session will provide basic information on using the Polycom system in support of our adult learners enrolled in distance education courses.
We will learn about the equipment, connect to site(s), adjust video and audio settings using the touch controls, and share content.
IT has supported video conferencing for 3 years. However, use of a multi conferencing bridge and touch controls are new to our campus. In addition, delivery of course content via video conferencing is new to Southern Wesleyan and will require ‘buy in’ at all levels to be successful.

## Slide 3: Training Outline
Lesson 1: Equipment
Lesson 2: Connecting and adjusting camera/audio settings
Lesson 3: Sharing Content
Lesson 4: Best Practices

## Slide 4: Lesson 1: Objectives
Familiarize users with all equipment at the remote learning centers.
  System should not move within the room or out of the room.
Discuss the purpose of the multi conferencing unit (MCU) on the main campus.
Plan B – Using telephone conferencing in the event of a network failure or equipment failure.
  Some work yet to be completed.

## Slide 5: Lesson 1: Equipment Used
Equipment used at each learning center.
  Codec – HDX 7000.
  HD Eagle Eye Camera.
  HDX Microphone
  User interface (Touch Screen, Remote)
  Display (dual 55 inch TV’s)

## Slide 6: Lesson 1: Equipment Used
Equipment used at each learning center.
  Codec – HDX 7000.
  HD Eagle Eye Camera.
  HDX Microphone
  User interface (Touch Screen, Remote)
  Display (dual 55 inch TV’s)

## Slide 7: Lesson 1: Equipment Used
Equipment used at each learning center.
  Codec – HDX 7000.
  HD Eagle Eye Camera.
  HDX Microphone
  User interface (Touch Screen, Remote)
  Display (dual 55 inch TV’s)
Notes: Remote receiver is in camera

## Slide 8: Lesson 1: Equipment Used
Equipment used at each learning center.
  Codec – HDX 7000
  HD Eagle Eye Camera
  HDX Microphone
  User interface (Touch Screen, Remote)
  Display (dual 55 inch TV’s)
Notes: Mute button. Where does it need to be located in the room

## Slide 9: Lesson 1: Equipment Used
Equipment used at each learning center.
  Codec – HDX 7000.
  Eagle Eye Camera.
  Microphone
  User interface (Touch Screen, Remote)
  Display (dual 55 inch TV’s)
Notes: Connections on the unit – USB for computer and Network for pairing device to codec POE necessary

## Slide 10: Lesson 1: Equipment Used
Equipment used at each learning center.
  Codec – HDX 7000.
  Eagle Eye Camera.
  Microphone
  User interface (Touch Screen, Remote)
  Display (dual 55 inch TV’s)
Notes: Power button and remote usage - only one remote is needed

## Slide 11: Lesson 1: Equipment Used
  RMX 2000 Multi Conferencing Unit
  The Polycom RMX 2000 is an advanced conferencing platform with intelligence built-in including dynamic resource allocation, network flexibility and reliability and cost-effective scalability, all tightly integrated with major UC partners to connect the most people in the highest quality at the lowest cost. Easy to set up, easy to use, and a powerful tool for collaboration, the Polycom RMX 2000 platform provides intuitive, high-quality multipoint conferencing to end users, as well as unparalleled flexibility and control to administrators.

## Slide 12: Lesson 1: Equipment Used
Placing Ad Hoc Conference Calls
    1. While on the first call, press the Conf button to place the call on hold. CALL NEXT PARTY TO CNF appears.
  2. Place a call to the next conference party. For external calls, press the Outgoing button or enter the Outgoing Call access code (8 is the default code), and then dial the number.
  3. After the party answers, announce the conference, and then press the Conf button to place the call on hold. If necessary, repeat this step to add the remaining conference party.
  4. Press the Conf button again to start the conference. CNF IN PROGRESS appears.

## Slide 13: Lesson 1: Wrap-up
Questions
Websites
  YouTube video - https://www.youtube.com/watch?v=3VTgDbiBMr4
  323 TV - http://www.323.tv/products/video-conferencing/conference-room/polycom-hdx-7000-720?gclid=COrN3vq6j8UCFcKIaQodQ4IAyA

## Slide 14: Lesson 2: Objectives
Understand how the equipment connects via point to point.
Understand how to connect using a conferencing bridge.
Use of the touch control screen.

## Slide 15: Lesson 2: Connecting Point to Point
Systems are not licensed for multi point but will connect to a single site.
Each HDX 7000 has a unique IP address that identifies it on the network. IP information is available by pressing the system icon.
10.xx.75.5 (Example only. IP is dynamically assigned)
How do I find my IP address?

## Slide 16: Lesson 2: Connecting to the MCU
Multi point licenses are controlled by the MCU and will manage 10 HD and 40 SD connections.
The RMX 2000 has numerous IP addresses used to manage the multiple connections.
Only IP address needed to connect to the MCU is 10.0.75.248
This is not published on the units but can be referenced under the recent calls section on the touch control unit.

## Slide 17: Lesson 2: Touch Control Basics
The touch control is powered by a POE network connection and is assigned an IP address.
Paired with the codec which disables the remote except for power on/off.
Swipe or touch navigation is available.
Content can be shared through the use of a USB stick or computer.
Cable safety is extremely important both for class participants and the equipment.

## Slide 18: Lesson 2: Touch Control Basics
Review of touch control buttons
  Call - Use this feature to connect to the MCU or point to point. Use IP address, address book or recent calls.
  Camera – Use this feature to adjust near and far cameras and set presets.
  Audio – Use this feature to adjust volume on codec. Audio is coming from the TV so volume should be set at 30 on TV and then adjusted from the touch control to appropriate level. Turn off volume leveling on TV.
  Settings – Use this icon to check IP address or other system information for touch control and HDX system.

## Slide 19: Lesson 2: Touch Control Basics
YouTube video - https://www.youtube.com/watch?v=P_kequ6RTBU

## Slide 20: Lesson 2: Wrap-up
Questions?

## Slide 21: Lesson 3: Sharing Content
Show how to share content from a PC
  www.polycom.com/ppcip
Show how to share content from a USB

## Slide 22: Lesson 3: Sharing Content from a PC
People+Content IP allows you to send content from a computer that is connected directly to the Touch Control.
Using the USB content cable, connect the computer directly to the underside of the Touch Control.
If autorun is enabled on the computer, you are prompted to run People+Content IP. If autorun is disabled on your computer, People+Content IP shows up as an external drive, and you must navigate to My Computer to launch it manually.
Launch People+Content IP.
Open the content you want to show, and click in People+Content IP.
Click in People+Content IP to stop showing content.

## Slide 23: Lesson 3: Sharing Content from a USB Drive
A Polycom Touch Control can show content stored on a USB drive. You can annotate the file while showing it to the far sites.
Connect the USB drive to the USB connector on the right side of the Polycom Touch Control.
From the Home screen or call screen, touch Show Content.
To view the files stored on a USB drive, touch the USB drive button.
  If another participant has People+Content IP connected to the HDX system to show content, that content must be stopped before the Polycom
Touch Control can show content from a USB drive.

## Slide 24: Lesson 3: Sharing Content from a USB Drive cont.
Navigate to the file that you want to show.
The Polycom Touch Control can open slideshows .pptx), documents (.pdf), and images (.bmp, .gif, .jpg, .png).
To browse by Name, File Type, or Date Modified, do the following:
  » Touch the tabs at the bottom of the screen.
  » Touch a tab again to reverse the sort order.
  » Touch a folder to open it.
  » Press to go back one level.
To filter by All Files, Recently Viewed Files, or type of file such as Slide Presentations, Documents, or Images, press .
To search for a file, touch the search field at the top of the screen.
Touch a folder to open it.
To view a file, touch it.

## Slide 25: Lesson 3: Wrap-up
Questions?

## Slide 26: Lesson 4: Tips for Great Meetings

## Slide 27: Lesson 4: Tips for Great Meetings
Make sure you have the IP address of the site you want to call or that the site is listed in a directory.
Set your camera presets before you start your call so that you can quickly use them during the call.
Use the "mute" button on the remote control when another site is speaking, and deactivate when you wish to speak.
Avoid "double talk"; allow the other site/person to finish speaking before you speak. Double talking may cause audio feedback and echo from the audio bridge.
Set up the equipment before the scheduled time so you will have time to test the system and resolve any issues before the meeting.

## Slide 28: Lesson 4: Tips for Great Video
Avoid wearing bright colors, all-light or all-dark clothing, or very "busy" patterns (such as small checks or narrow stripes).
Light pastels and muted colors look the best on the screen.
If there are windows in the room, close any drapes or blinds. Daylight is a variable light source and can conflict with interior room lighting.
Use natural gestures when you speak.
When adjusting your camera, try to fill the screen as much as possible with people rather than with the table, chairs, walls, lights, or the floor.

## Slide 29: Lesson 4: Tips for Great Audio
Speak in your normal voice, without shouting.
Ask the people at the other site if they can hear you.
Have them introduce themselves so you can be sure that you can hear them.
Mute the microphone before moving it during a meeting.
Since the audio has a very slight delay, you may want to pause briefly for others to answer you or to make comments.
As with any meeting, try to limit side conversations.
Place the microphone on the table in front of the people in the meeting.

## Slide 30: Lesson 4: Tips for Multi-point Conferencing
The Multi-point Bridge is responsible for the video switching in a voice-activated multi-point. It switches automatically among the conference sites depending on who is speaking.
Your voice will activate the Multi-point Bridge, which will change the picture from the last person who spoke to the person currently speaking.

## Slide 31: Lesson 4: Tips for Sharing Content
Check that your computer has the application you need to show your documents, such as Microsoft PowerPoint, Project, or Word.
For a smoother presentation, make sure your presentation is ready to show. Test it before you start the call.
If you choose to use the touch control content sharing via USB, remember that this takes some time to load into the memory for display,

## Slide 32: Summary of Training
Handouts are available on mySWU in the Information Technology section

## Slide 33: Assessment and Evaluation
Was the training helpful?
Suggestions for improvement.